For building
rosdep install --from-paths src --ignore-src -r -y

colcon build --symlink-install --cmake-args -DCMAKE_BUILD_TYPE=RelWithDebInfo

------------------------------------------------------------------------------------

Run EC driver as node:
ros2 launch metavision_driver driver_node.launch.py
event_message_size_threshold:=xxx

*Run EC driver as composable node:
ros2 launch metavision_driver driver_composition.launch.py

Run EC renderer: from event to event_image
ros2 launch event_camera_renderer renderer.launch.py

------------------------------------------------------------------------------------

EC driver custom parameters description (see all in metavision_driver github):

event_message_size_threshold: (in bytes) minimum size of events (in bytes) to be aggregated in one ROS event message before message is sent. Defaults to 1MB.

Dynamic reconfiguration parameters (https://docs.prophesee.ai/stable/hw/manuals/biases.html)

- bias_diff_on: determines the ON contrast threshold, the factor by which the pixel must get brighter, before an ON event occurs for that pixel.
- bias_diff_off: determines the OFF contrast threshold, the factor by which the pixel must get darker, before an OFF event occurs for that pixel.
- bias_fo: adjusts the low-pass filter, which changes how rapidly fluctuating light is filtered out. It determines the maximum rate of change of illumination that can be detected.
- bias_hpf: adjusts the high-pass filter, which determines how slow illumination change is filtered out. It determines the minimum rate the light must change, for the pixel to output an event.
bias_refr: adjusts the refractory period, which determines the duration for which the pixel is blind after each event.

------------------------------------------------------------------------------------

EC Node with composition for reading events, spatio-temporal filtering and image reconstruction publishing: